# UAIR_BSP_Flash

## Global defines
### BSP_FLASH_PAGE_SIZE_BITS
Size, in number of bits, of each page. Each page will be 2BSP_FLASH_SIZE_BITS bytes long. See [BSP_FLASH_PAGE_SIZE].
### BSP_FLASH_PAGE_SIZE
Size, in bytes, of each page. See [BSP_FLASH_PAGE_SIZE_BITS]
## Types
### flash_page_t
Page index. 8-bit unsigned integer.
### flash_address_t
Flash address. 32-bit unsigned integer. This address (addresing bytes) is relative to the area, not a global address.
### flash_error_e
Enumerated type with error types for BSP errors.
## UAIR_BSP_flash_config_area_get_page_count
BSP_FLASH_REQ_100
[UAIR_BSP_flash_config_area_get_page_count] shall return the number of 2KB pages allocated and available for config storage.
## UAIR_BSP_flash_config_area_erase_page
BSP_FLASH_REQ_200
[UAIR_BSP_flash_config_area_erase_page] shall return [BSP_ERROR_NONE] and erase the [page] if a valid page has been specified and no errors occur in the erase process.
BSP_FLASH_REQ_201
[UAIR_BSP_flash_config_area_erase_page] shall return [BSP_ERROR_WRONG_PARAM] and skip erase if [page] is not within the allocated range 0 to [UAIR_BSP_flash_config_area_get_size_pages()]-1.
BSP_FLASH_REQ_208
[UAIR_BSP_flash_config_area_erase_page] shall unlock the flash prior to erase.
BSP_FLASH_REQ_209
[UAIR_BSP_flash_config_area_erase_page] shall, if the flash was previously unlocked. lock the flash before exiting.
BSP_FLASH_REQ_202
[UAIR_BSP_flash_config_area_erase_page] shall return [BSP_ERROR_PERIPH_FAILURE] and skip erase if the flash could not be unlocked.
BSP_FLASH_REQ_203
[UAIR_BSP_flash_config_area_erase_page] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_UNLOCK] if the flash could not be unlocked.
BSP_FLASH_REQ_204
[UAIR_BSP_flash_config_area_erase_page] shall return [BSP_ERROR_PERIPH_FAILURE] if the flash erase was successful but the flash could not be locked after erase.
BSP_FLASH_REQ_205
[UAIR_BSP_flash_config_area_erase_page] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_LOCK] if the flash could not be locked after erase.
BSP_FLASH_REQ_206
[UAIR_BSP_flash_config_area_erase_page] shall return [BSP_ERROR_PERIPH_FAILURE] if the [page] could not be erased by the low-level routines.
BSP_FLASH_REQ_207
[UAIR_BSP_flash_config_area_erase_page] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_ERASE] and [value]=[physical_page] if the page could not be erased, where [physical_page] corresponds to the absolute page in flash where the error was detected.

## UAIR_BSP_flash_config_area_read
BSP_FLASH_REQ_300
[UAIR_BSP_flash_config_area_read] shall return [len_bytes] and read the contents of the config area space starting at address [address] into the target area [dest] if [address] and [address+len_bytes-1] fall within the config address space.
Note: [address] is relative and starts at 0x0, extending up to the maximum area of the config space.
BSP_FLASH_REQ_301
[UAIR_BSP_flash_config_area_read] shall return the number of “available bytes” and read the contents of the config area space starting at address [address] into the target area [dest] with size “available bytes” if [address] falls within the config address space, but [address+len_bytes] extend beyond the allocated config address space. “available bytes” is defined as the amount of data between [address] and the end of the config address space.
BSP_FLASH_REQ_302
[UAIR_BSP_flash_config_area_read] shall return [BSP_ERROR_WRONG_PARAM] if [address] does not fall within the config address space.
## UAIR_BSP_flash_config_area_write
BSP_FLASH_REQ_400
[UAIR_BSP_flash_config_area_write] shall return [count_doublewords] and write [count_doublewords] doublewords [64-bit each] from [data] array into config area at address [address] if [address] is a valid 64-bit aligned address and [address] and [address+count_doublewords-1] fall within the allocated config area, and no flash errors are detected.
Note: [address] is relative and starts at 0x0, extending up to the maximum area of the config space.
Note: flash errors are either unlock operation failures or programnming operation failures.
BSP_FLASH_REQ_401
[UAIR_BSP_flash_config_area_write] shall return [BSP_ERROR_WRONG_PARAM] if [address] is not 64-bit aligned.
BSP_FLASH_REQ_410
[UAIR_BSP_flash_config_area_write] shall return [BSP_ERROR_WRONG_PARAM] if [address] is not within config space allocated range
BSP_FLASH_REQ_402
[UAIR_BSP_flash_config_area_write] shall return “doublewords” and write “doublewords” doublewords [64-bit each] from [data] array into config area at address [address] if [address] is a valid 64-bit aligned address and [address] falls within the allocated config area, but [address+count_doublewords-1] extend beyond the allocated config area space, and no flash errors are detected. “doublewords” is defined by the amount of doublewords between [address] and the end of the allocated config area space.
BSP_FLASH_REQ_403
[UAIR_BSP_flash_config_area_write] shall return [BSP_ERROR_PERIPH_FAILURE] and not perform any write if the flash could not be locked.
BSP_FLASH_REQ_404
[UAIR_BSP_flash_config_area_write] shall return [BSP_ERROR_PERIPH_FAILURE] if the flash could not be locked after a successful write .
BSP_FLASH_REQ_405
[UAIR_BSP_flash_config_area_write] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_LOCK] if the flash could not be locked after programming.
BSP_FLASH_REQ_406
[UAIR_BSP_flash_config_area_write] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_UNLOCK] if the flash could not be unlocked prior to programming.
BSP_FLASH_REQ_407
[UAIR_BSP_flash_config_area_write] shall return [BSP_ERROR_PERIPH_FAILURE] if any programming error occurs while programming the flash.
Note: in the event of a programming error the requested area (from [address] extending [count_doublewords]) might have been partially programmed.
BSP_FLASH_REQ_411
[UAIR_BSP_flash_config_area_write] shall raise an BSP_error with [zone]=[BSP_ZONE_FLASH] and [type]= [BSP_ERROR_TYPE_FLASH_PROGRAM] if a problem was detected when programming.
BSP_FLASH_REQ_408
[UAIR_BSP_flash_config_area_write] shall unlock the flash prior to programming.
BSP_FLASH_REQ_409
[UAIR_BSP_flash_config_area_write] shall, if the flash was previously unlocked, lock the flash before exiting.